## Slide 1
BLDC HSR Ver. 3.1
At DPC-11, All functions except EPA & Continuous Speed Mode are same with other BLDC Servos (HSB-93xx)
Continuous speed mode
1) On : Turn on “Continuous speed mode” of BLDC HSR servo.
- At 1500 us, the servo stops.
- At 2100 us, the servo travels in a clockwise direction. (CW)
- At 900 us, the servo travels in a counter clockwise direction. (CCW)
2) Off: Turn off. The servo travels based on EPA setup.

## Slide 2
EPA
1) CW / CCW : Setup the angle of HSR servo.
ex) CW = 50, CCW = 100 setup
At 2100us : The servo rotates 50° in a clockwise direction. (CW)
At 900us : The servo rotates 100° in a counter clockwise direction (CCW)
* In proportion to Travel Multiplier, the setting range (Min, Max) is changed.
2) Neut. : Setup the neutral position (1500us) of HSR servo.
- 1° step setup available among the whole 360° range.
3) Travel Multiplier : Setup the angle range.
- 1~10 step can be selected. Each 1 step makes about twice angle range.
* To apply the setup, please make sure to click “Apply” button.